Protecto Wrap Co.

1955 South Cherokee St.

Denver, CO 80223

Phone: (800) 759-9727

Phone: (303) 777-3001

Fax: (303) 777-9273

E-mail: info@protectowrap.com

www.protectowrap.com

This MANU-SPEC utilizes the Construction Specifications Institute (CSI) Project Resource Manual (PRM), including MasterFormatTM, SectionFormatTM and PageFormatTM. A MANU-SPEC is a manufacturer-specific proprietary product specification using the proprietary method of specifying applicable to project specifications and master guide specifications. Optional text is indicated by brackets []; delete optional text in final copy of specification. Specifier Notes typically precede specification text; delete notes in final copy of specification. Trade/brand names with appropriate symbols typically are used in Specifier Notes; symbols are not used in specification text. Metric conversion, where used, is soft metric conversion.

This MANU-SPEC specifies AFM and AFM-WM peel-and-stick anti-fracture and waterproof anti-fracture membranes for use under ceramic tile, porcelain, and natural stone for stress relief and waterproofing. These products are manufactured by Protecto Wrap Co. Revise MANU-SPEC section number and title below to suit project requirements, specification practices and section content. Refer to CSI MasterFormat for other section numbers and titles.

SECTION 093000 - TILING

GENERAL

SUMMARY

Section Includes: Anti-fracture and anti-fracture waterproofing membranes.

Related Sections:

Tile and Tile Installation: Division 09 tile sections.

REFERENCES

ASTM International:

ASTM C627 Standard Test Method for Evaluating Ceramic Floor Tile Installation Systems Using the Robinson-Type Floor Tester.

ASTM D412 Standard Test Methods for Vulcanized Rubber and Thermoplastic Elastomers-Tension.

ASTM E90 Standard Test Method for Laboratory Measurement of Airborne Sound Transmission Loss of Building Partitions and Elements.

ASTM E492 Standard Test Method for Laboratory Measurement of Impact Sound Transmission Through Floor-Ceiling Assemblies Using the Tapping Machine.

Tile Council of North America (TCNA):

Handbook for Ceramic Tile Installation.

SUBMITTALS

General: Submit listed submittals in accordance with Conditions of the Contract and Division 01 Submittal Procedures Section.

Product Data: Submit product data, including manufacturer's SPEC-DATA sheet, for specified products.amples: Submit 6 inch x 6 inch (152 x 152 mm) samples of

QUALITY ASSURANCE

Regulatory Requirements and Approvals: [Specify applicable requirements of regulatory agencies.].

[Code agency name].

[Report or approval number].

DELIVERY, STORAGE & HANDLING

General: Comply with Division 01 Product Requirements Section.

Delivery: Deliver materials in manufacturer's original, unopened, undamaged containers with identification labels intact.

Storage and Protection: Store materials protected from exposure to harmful environmental conditions and at temperature and humidity conditions recommended by the manufacturer.

WARRANTY

Project Warranty: Refer to Conditions of the Contract for project warranty provisions.

Manufacturer's Warranty: Submit, for Owner's acceptance, manufacturer's standard warranty document executed by authorized company official. Manufacturer's warranty is in addition to, and not a limitation of, other rights Owner may have under Contract Documents.

Warranty Period: 5 years commencing on Date of Substantial Completion.

PRODUCTS

MEMBRANE(S)

Manufacturer: Protecto Wrap Co.

Contact: 1955 South Cherokee St., Denver, CO 80223; Telephone: (800) 759-9727, (303) 777-3001; Fax: (303) 777-9273; E-mail: info@protectowrap.com; website: www.protectowrap.com.

Substitutions: No substitutions permitted.

MATERIALS

Membrane Physical Properties:

Thickness: 40 mils (1 mm).

Elongation (ASTM D412): 500%, minimum, (rubberized adhesive only).

Robinson Floor Test (ASTM C627): Rated for extra heavy traffic.

Impact Insulation Class (ASTM E492): IIC 67.

Sound Transmission Class (ASTM E90): STC 55.

Anti-Fracture Membrane: AFM.

Anti-Fracture Waterproofing Membrane: AFM-WM.

ACCESSORIES

Adhesive: No. 6000 Water-Based Primer.

No. 80 Primer.

JS160 Mastic.

AFM 500 Detail Tape.

EXECUTION

MANUFACTURER'S INSTRUCTIONS

Compliance: Comply with manufacturer's product data, including product technical bulletins, product catalog installation instructions, waterproofing details and product carton instructions for installation.

EXAMINATION

Site Verification of Conditions: Verify that substrate conditions, which have been previously installed under other sections, are acceptable for product installation in accordance with manufacturer's instructions.

PREPARATION

Prepare surfaces using the methods recommended by the manufacturer for achieving the best result for the substrate under the project conditions.

INSTALLATION

Specifier Note: Retain paragraphs below if required to conform to project requirements.

Plywood Subfloors: In accordance with TCA Method F147.

Expansion Joints: In accordance with TCA Method EJ171.

FIELD QUALITY CONTROL

Specifier Note: Retain below if waterproof membrane is specified; manufacturer will not issue a warranty unless the installation passes this test.

Flood Test: Test waterproofing membrane applications prior to installation of tile in accordance with the manufacturer's test procedures. Proof of successful water testing is required for warranty on waterproofing applications.

END OF SECTION