Protecto Wrap Co.

1955 South Cherokee St.

Denver, CO 80223

Phone: (800) 759-9727

Phone: (303) 777-3001

Fax: (303) 777-9273

E-mail: info@protectowrap.com

www.protectowrap.com

This MANU-SPEC utilizes the Construction Specifications Institute (CSI) Project Resource Manual (PRM), including MasterFormatTM, SectionFormatTM and PageFormatTM. A MANU-SPEC is a manufacturer-specific proprietary product specification using the proprietary method of specifying applicable to project specifications and master guide specifications. Optional text is indicated by brackets []; delete optional text in final copy of specification. Specifier Notes typically precede specification text; delete notes in final copy of specification. Trade/brand names with appropriate symbols typically are used in Specifier Notes; symbols are not used in specification text. Metric conversion, where used, is soft metric conversion.

This MANU-SPEC specifies Protective Sill Drainage System (PSDS), a sill drainage system composed of positive sloped, closed-cell foam with a back dam. This product is manufactured by Protecto Wrap Co. Revise MANU-SPEC section number and title below to suit project requirements, specification practices and section content. Refer to CSI MasterFormatTM for other section numbers and titles.

SECTION 076526 - SELF-ADHERING SHEET FLASHING

GENERAL

SUMMARY

Section Includes: Sill drainage system.

REFERENCES

ASTM International (ASTM):

ASTM D779 Standard Test Method for Water Resistance of Paper, Paperboard, and Other Sheet Materials by the Dry Indicator Method.

ASTM D822 Standard Practice for Filtered Open-Flame Carbon-Arc Exposures of Paint and Related Coatings.

ASTM E84 Standard Test Method for Surface Burning Characteristics of Building Materials.

ASTM E96 Standard Test Methods for Water Vapor Transmission of Materials.

ASTM E283 Standard Test Method for Determining Rate of Air Leakage Through Exterior Windows, Curtain Walls, and Doors Under Specified Pressure Differences Across the Specimen.

ASTM E331 Standard Test Method for Water Penetration of Exterior Windows, Skylights, Doors, and Curtain Walls by Uniform Static Air Pressure Difference.

ASTM E547 Standard Test Method for Water Penetration of Exterior Windows, Skylights, Doors, and Curtain Walls by Cyclic Static Air Pressure Difference.

Technical Association of the Pulp and Paper Industry (TAPPI):

T460 Air Resistance of Paper (Gurley Method).

SYSTEM DESCRIPTION

Performance Requirements:

Air Infiltration: Less than 0.01 cfm per square foot when tested with vinyl or wood windows, wind speed of 50 mph (81 kph), in accordance with ASTM E283.

Water Penetration: As follows when tested in accordance with ASTM E331 and E547 at a test pressure of 2.86 psf:

Vinyl Windows: Not less than 7.50 psf.

Wood Windows: Not less than 8.25 psf.

Fire Performance of House Wrap:

Surface burning characteristics when tested in accordance ASTM E84:

Flamespread: 25, maximum.

Smoke Developed: 450, maximum.

SUBMITTALS

General: Submit listed submittals in accordance with Conditions of the Contract and Division 01 Submittal Procedures Section.

Product Data: Submit product data, including manufacturer's SPEC-DATA sheet, for specified products.

Samples: Submit 6 inch (152 mm) samples of specified flashing.

QUALITY ASSURANCE

Regulatory Requirements: In accordance with Section [01 41 00 - Regulatory Requirements] [______].

DELIVERY, STORAGE & HANDLING

General: Comply with Division 01 Product Requirements Section.

Delivery: Deliver materials in manufacturer's original, unopened, undamaged containers with identification labels intact.

Storage and Protection: Store materials protected from exposure to harmful environmental conditions and at temperature and humidity conditions recommended by the manufacturer.

WARRANTY

Project Warranty: Refer to Conditions of the Contract for project warranty provisions.

Manufacturer's Warranty: Submit in accordance with Section [01 78 36 - Warranties] [______] for Owner's acceptance, manufacturer's standard warranty document executed by authorized company official. Manufacturer's warranty is in addition to, and not a limitation of, other rights Owner may have under Contract Documents.

Warranty Period: 15 years commencing on Date of Substantial Completion.

PRODUCTS

SELF-ADHERING SHEET FLASHING

Manufacturer: Protecto Wrap Co.

Contact: 1955 South Cherokee St., Denver, CO 80223; Telephone: (800) 759-9727, (303) 777-3001; Fax: (303) 777-9273; E-mail: info@protectowrap.com; website: www.protectowrap.com.

Protecto Sill Drainage System (PSDS): Positive sloped, closed-cell foam with a back dam.

ACCESSORIES

BT Primer: High tack primer.

Protecto-Tak Spray Adhesive: Spray applied high tack primer.

Protecto Sealant 25XL: One-part, moisture cure polyurethane.

PSDS Detail Tape: 60 mil (1.5 mm) unreinforced tape.

BT25XL Building Tape: 25 mil (0.64 mm) self-adhering air/vapor barrier tape.

Protecto Flex: 60 mil (1.5 mm) self-adhering flashing tape.

Dri-Shield Housewrap:

Tensile Strength: As follows when tested in accordance with ASTM D822:

Machine Direction: 50 psi.

Cross Direction: 46 psi.

Air Porosity: As follows when tested in accordance with TAPPI T-460:

Side A-B: Not less than 9.4 seconds per 100 cm3.

Side B-A: Not less than 9.1 seconds per 100 cm3.

Water Resistance: As follows when tested in accordance with ASTM D779:

Side A-B: Not less than 2 hours, 47 minutes, 30 seconds.

Side B-A: Not less than 1 hour, 52 minutes, 42 seconds.

Water Vapor Permeance: 7.5, average, when tested in accordance with ASTM E96.

Dri-Shield Sealing Tape.

PRODUCT SUBSTITUTIONS

Substitutions: Substitutions in accordance with Section [01 25 13 - Product Substitution Procedures] [No substitutions permitted] [______].

EXECUTION

Specifier Note: Paragraph below is an addition to CSI SectionFormat and a supplement to MANU-SPEC. Retain or delete paragraph below per project requirements and specifier's practice.

MANUFACTURER'S INSTRUCTIONS

Compliance: Comply with manufacturer's product data, including product technical bulletins, product catalog installation instructions and product carton instructions for installation.

EXAMINATION

Site Verification of Conditions: Verify that substrate conditions, which have been previously installed under other sections, are acceptable for product installation in accordance with manufacturer's instructions.

PREPARATION

Prepare surfaces using the methods recommended by the manufacturer for achieving the best result for the substrate under the project conditions.

END OF SECTION