Protecto Wrap Co.

1955 South Cherokee St.

Denver, CO 80223

Phone: (800) 759-9727

Phone: (303) 777-3001

Fax: (303) 777-9273

E-mail: info@protectowrap.com

www.protectowrap.com

This MANU-SPEC utilizes the Construction Specifications Institute (CSI) Project Resource Manual (PRM), including MasterFormatTM, SectionFormatTM and PageFormatTM. A MANU-SPEC is a manufacturer-specific proprietary product specification using the proprietary method of specifying applicable to project specifications and master guide specifications. Optional text is indicated by brackets []; delete optional text in final copy of specification. Specifier Notes typically precede specification text; delete notes in final copy of specification. Trade/brand names with appropriate symbols typically are used in Specifier Notes; symbols are not used in specification text. Metric conversion, where used, is soft metric conversion.

This MANU-SPEC specifies PW-100/40, a peel-and-stick membrane air and vapor barrier for use as a full building wrap or for sealing building joints. This product is manufactured by Protecto Wrap Co. Revise MANU-SPEC section number and title below to suit project requirements, specification practices and section content. Refer to CSI MasterFormat for other section numbers and titles.

SECTION 072600 - VAPOR RETARDERS

GENERAL

REFERENCES

ASTM International:

ASTM D146 Standard Test Methods for Sampling and Testing Bitumen-Saturated Felts and Woven Fabrics for Roofing and Waterproofing.

ASTM D412 Standard Test Methods for Vulcanized Rubber and Thermoplastic Elastomers-Tension.

ASTM E96 Standard Test Methods for Water Vapor Transmission of Materials.

ASTM E154 Standard Test Methods for Water Vapor Retarders Used in Contact with Earth Under Concrete Slabs, on Walls, or as Ground Cover.

ASTM E283 Standard Test Method for Determining Rate of Air Leakage Through Exterior Windows, Curtain Walls, and Doors Under Specified Pressure Differences Across the Specimen.

SUBMITTALS

General: Submit listed submittals in accordance with Conditions of the Contract and Division 01 Submittal Procedures Section.

Product Data: Submit product data, including manufacturer's SPEC-DATA sheet, for specified products.

Samples: Submit 6 inch x 6 inch (152 x 152 mm) samples of specified membrane(s).

QUALITY ASSURANCE

Regulatory Requirements and Approvals: [Specify applicable requirements of regulatory agencies.].

[Code agency name].

[Report or approval number].

DELIVERY, STORAGE & HANDLING

General: Comply with Division 01 Product Requirements Section.

Delivery: Deliver materials in manufacturer's original, unopened, undamaged containers with identification labels intact.

Storage and Protection: Store materials protected from exposure to harmful environmental conditions and at temperature and humidity conditions recommended by the manufacturer.

WARRANTY

Project Warranty: Refer to Conditions of the Contract for project warranty provisions.

Manufacturer's Warranty: Submit, for Owner's acceptance, manufacturer's standard warranty document executed by authorized company official. Manufacturer's warranty is in addition to, and not a limitation of, other rights Owner may have under Contract Documents.

Warranty Period: 5 years commencing on Date of Substantial Completion.

PRODUCTS

AIR/VAPOR BARRIER

Manufacturer: Protecto Wrap Co.

Contact: 1955 South Cherokee St., Denver, CO 80223; Telephone: (800) 759-9727, (303) 777-3001; Fax: (303) 777-9273; E-mail: info@protectowrap.com; website: www.protectowrap.com.

Substitutions: No substitutions permitted.

MATERIALS

Composition: SBS modified, rubberized asphalt sheet waterproofing membrane with polyethylene topping.

PW-100/40, 40 mils (1 mm) thick.

Pliability (ASTM D146): Unaffected when bent 180 degrees over a 1 inch (25.4 mm) mandrel at -25 degrees F (-32 degrees C).

Tensile Strength (Membrane) (ASTM D412 (Die C) Modified): Not less than 250 psi (1.7 MPa).

Elongation to Ultimate Failure (ASTM D412 (Die C) Modified): Not less than 300%.

Puncture Resistance (ASTM E154): Not less than 40 lb (178 N) when stretched by blunt object.

Permeance of In-Place System (ASTM E283): Not more than 0.25 cubic feet per minute per square foot (0.01 l/s/m2) when tested with a pressure difference of 75 Pa.

Resistance to 2 kPa Air Pressure Difference (ASTM E283): No increase in equivalent leakage area.

Permeance - Metric Perms (ASTM E96 (Method B)): Not more than 0.009 perm (0.517 ng/(Pa x s x m2)).

PW-100/60, 60 mils (1.5 mm) thick.

Pliability (ASTM D146): Unaffected when bent 180 degrees over a 1 inch (25.4 mm) mandrel at -25 degrees F (-32 degrees C).

Tensile Strength (Membrane) (ASTM D412 (Die C) Modified): Not less than 250 psi (1.7 MPa).

Elongation to Ultimate Failure (ASTM D412 (Die C) Modified): Not less than 300%.

Puncture Resistance (ASTM E154): Not less than 40 lb (178 N) when stretched by blunt object.

Permeance of In-Place System (ASTM E283): Not more than 0.25 cubic feet per minute per square foot (0.01 l/s/m2) when tested with a pressure difference of 75 Pa.

Resistance to 2 kPa Air Pressure Difference (ASTM E283): No increase in equivalent leakage area.

Permeance - Metric Perms (ASTM E96 (Method B)): Not more than 0.009 perm (0.517 ng/(Pa x s x m2)).

ACCESSORIES

No. 100 Primer.

No. 100 VOC Primer.

No. 6000 Water-Based Primer.

Protecto Sealant 25XL.

JS160H Mastic.

EXECUTION

Specifier Note: Paragraph below is an addition to CSI SectionFormat and a supplement to MANU-SPEC. Retain or delete paragraph below per project requirements and specifier's practice.

MANUFACTURER'S INSTRUCTIONS

Compliance: Comply with manufacturer's product data, including product technical bulletins, product catalog installation instructions and product carton instructions for installation.

EXAMINATION

Site Verification of Conditions: Verify that substrate conditions, which have been previously installed under other sections, are acceptable for product installation in accordance with manufacturer's instructions.

PREPARATION

Prepare surfaces using the methods recommended by the manufacturer for achieving the best result for the substrate under the project conditions.

END OF SECTION